## Slide 1: Azure IoT Device Model “SAM-IoT-Wx-v2” Version 1
Wireless Specialist (PACNW)
Randy Wu, Principal ESE

## Slide 2: “SAM-IoT-WM” V2: Connecting an Application MCU
Azure Cloud
Application
MCU
UART (9600 baud)
SPI (30 kHz)
CLI
DTI
FUNC | DIR | PIN | HEADER
TXD |  | PB02 | N/A
RXD |  | PB03 | N/A
MOSI |  | PA04 | J20-6
SCK |  | PA05 | J20-4
CS |  | PA06 | J20-3
SPI
UART
MQTT
GOAL
Extend the “SAM-IoT-WM” Version 1 device model with additional interfaces to accommodate telemetry, properties, and commands for connecting an external application MCU
NEW

## Slide 3: Additional Interfaces for “SAM-IoT-Wx-v2” Version 1
Azure Cloud
Telemetry
Brightness
Temperature
Button events
Properties
Blue LED state
Green LED state
Yellow LED state
Red LED state
Telemetry interval
Commands
Reboot
Azure Device Model
(“SAM_IoT_Wx_v2; ”)
SAM-IoT Board
Sensors
- Light
- Temperature
4 LEDs
2 Buttons
Integers (4)
Strings (4)
Boolean (1)
Doubles (2)
Floats (2)
Long (1)
NEW
Integers – read only by cloud (2)
Integers – writable by cloud (2)
IP Address (read only string)
WINC1510 FW Version (read only string)
NEW
Send ASCII Message
NEW
1
MQTT

## Slide 4: Application Parameters – Direction of Data Flow
Azure Cloud
Telemetry
Brightness
Temperature
Button events
Properties
Blue LED state
Green LED state
Yellow LED state
Red LED state
Telemetry interval
Commands
Reboot
Azure Device Model
(“SAM_IoT_Wx_v2;1”)
SAM-IoT Board
Sensors
- Light
- Temperature
4 LEDs
2 Buttons
Integers – read only by cloud (2)
Integers – writable by cloud (2)
Integers (4)
Strings (4)
Boolean (1)
Doubles (2)
Floats (2)
Long (1)
Send ASCII Message
MQTT
Strings (IP Addr & FW ver) – read only

## Slide 5: Command Line Interface (CLI) for SAM-IoT
MQTT
Azure Cloud
Application MCU
UART (9600 baud)
Telemetry Reported to Cloud
Properties Sync’d with Cloud
Update Telemetry & Properties using ASCII commands via Command Line Interface (CLI)
CDC Interface (1200 to 500K baud)

## Slide 6: Standard ASCII Commands for SAM-IoT CLI
Help
Command Format | Action
idscope [ID Scope] | Get and set Azure DPS ID Scope
reconnect | MQTT reconnect
wifi –set <ssid>[,<pass>,[authType]] | Set Wi-Fi credentials (authType: 1 = Open, 2 = WPA, 3 = WEP)
wifi –[scan¦status] | Get list of Wi-Fi SSID’s or connection status
cloud -status | Get cloud connection status
key | Get ECC public key
device | Get ECC serial number
cli_version | Get CLI version
version | Get MCU application firmware version
debug [level] | Get and set debug level
reset | Reset host
q | Quit command processor
help | Help menu
NEW
Notes: Connection status – error in communication?

## Slide 7: CLI Responses for [wifi & cloud] commands
>wifi -scan
Action | CLI Response
Get list of all SSID’s currently in range | <SSID_1>,<SSID_2>,..,<SSID_N>
>wifi -status
Wi-Fi Connection Status | CLI Response
Disconnected | 0.0.0.0
Connected | <IP_Addr>,<SSID>
>cloud -status
Cloud Connection Status | CLI Response
Disconnected | false
Connected | true

## Slide 8: Application Command using CLI [telemetry]
index | description | name | schema | CLI Example | Action / Result
0 | Reset DTI command buffer |  |  | >telemetry 0,0 | Recommended before sending out a DTI data frame
1 | App Telemetry signed integer #1 | telemetry_Int_1 | integer | >telemetry 1,FE | telemetry_Int_1 = 254
2 | App Telemetry signed integer #2 | telemetry_Int_2 | integer | >telemetry 2,BA6E | telemetry_Int_2 = 47,726
3 | App Telemetry signed integer #3 | telemetry_Int_3 | integer | >telemetry 3,609D64 | telemetry_Int_3 = 6,331,748
4 | App Telemetry signed integer #4 | telemetry_Int_4 | integer | >telemetry 4,C36941E5 | telemetry_Int_4 = -1,016,512,027
5 | App Telemetry double #1 | telemetry_Dbl_1 | double | >telemetry 5,F537A021CF015B44 | telemetry_Dbl_1 = -4.43422395117885722194330763894E256
6 | App Telemetry double #2 | telemetry_Dbl_2 | double | >telemetry 6,9D1F2C043A774B55 | telemetry_Dbl_2 = 1.0367692620813990098267580227E-305
7 | App Telemetry float #1 | telemetry_Flt_1 | float | >telemetry 7,418345E1 | telemetry_Flt_1 = 16.40912
8 | App Telemetry float #2 | telemetry_Flt_2 | float | >telemetry 8,C20508DE | telemetry_Flt_2 = -33.25866
9 | App Telemetry Long | telemetry_Lng | long | >telemetry 9,CAFE1234BEEF5678 | telemetry_Lng = 14,627,148,657,496,905,336
10 | App Telemetry Boolean | telemetry_Bool | boolean | >telemetry 10,true | telemetry_Bool = true
11 | App Telemetry String #1 | telemetry_Str_1 | string | >telemetry 11,hello | telemetry_Str_1 = hello\0
12 | App Telemetry String #2 | telemetry_Str_2 | string | >telemetry 12,goodbye | telemetry_Str_2 = goodbye\0
13 | App Telemetry String #3 | telemetry_Str_3 | string | >telemetry 13,Hi!!! | telemetry_Str_3 = Hi!!!\0
14 | App Telemetry String #4 | telemetry_Str_4 | string | >telemetry 14,Bye!!! | telemetry_Str_4 = Bye!!!\0
Command: “telemetry”
Application MCU transmits its own telemetry updates using one of the storage slots in the table by choosing the desired index
> telemetry <index>,<data>
NEW

## Slide 9: Enhancement: Dedicated Telemetry Interface (SPI)
Application MCU
(SPI Master)
CS (PA06)
SCK (PA05)
MOSI (PA04)
MQTT
Azure Cloud
SAM-IoT
(SPI Slave)
Command Byte | Index Byte | Length (MSB) | Length (LSB) | Data Byte 1 | . . . . . . . | Data Byte N
Command = ASCII char ‘T’ or ‘t’ (hex value 0x54 or 0x74)
Index is defined by parameter table of the CLI telemetry command
Length (16-bit word) = total # of bytes in the payload
Max frame length = (4B header + 1024B max payload) bytes = 1028 bytes
Header
Payload
Data Frame
Notes: 1. (5000 milliseconds / 2048 Words) = 2.44 msec per update
2. (5000 milliseconds / 1024 Integers) = 4.88 msec per update

## Slide 10: Test Platform for Dedicated Telemetry Interface (SPI)
SPI Master (PIC-IoT)
https://github.com/randywu763/MCHP-IoT_SPI
SPI Slave
(SAM-IoT)
AN
RST
CS
SCK
MISO
MOSI
+3.3V
GND
AN
RST
CS
SCK
MISO
MOSI
+3.3V
GND
PA02
PA03
PA06
PA05
PA07
PA04
RB14
RB15
RA0
RA1
RB0
RB1
Mikro
BUS
Mikro
BUS
SAMD21
G18A
PIC24
FJ128
GA705
1. Press the SW1 Button
2. Red LED Toggles
3. Yellow LED Toggles
Notes: 1. (5000 milliseconds / 2048 Words) = 2.44 msec per update
2. (5000 milliseconds / 1024 Integers) = 4.88 msec per update

## Slide 11: Application Command using CLI [property]
index | description | name | schema | writable (by Cloud)
1 | App Property #1 | property_1 | integer | false
2 | App Property #2 | property_2 | integer | false
3 | App Property #3 | property_3 | integer | true
4 | App Property #4 | property_4 | integer | true
> property <index>,<data(hex)>
CLI Examples
Update Property #1 with a bitmask of 01110100b
> property 1,76
Update Property #3 with a value of 20,000
> property 3,4E20
Confirm that new value of Property #4 has been changed to 51,996 (after receiving the change request from the SAM-IoT)
> property 4,CAFE
Command: “property”
Application MCU communicates information about itself (e.g. state or configuration) using any of the properties (which can be read by the cloud on demand whenever needed). If the property is defined as writable by the cloud, this means the cloud is also allowed to change the value. In this case, the property command is also used as a confirmation response message (i.e. serving as an ACK to the SAM-IoT which will then send an ACK to the cloud).
NEW

## Slide 12: Property Write from the Cloud (writable = true)
Azure Cloud
Application MCU
1. Send New Property Value
4. Send ACK to complete sync
Writable properties can be changed from the Cloud
SAM will notify APP of the updated property by sending an ASCII message on the CLI PROP<x>=<new_value(hex)> (e.g. “PROP3=BEEF”)
Application must confirm the change using the property command as the ACK response
2. Send New Property Value
PROP<x>=<new_val(hex)>
3. Send Confirmation (ACK)
property <x>,<new_val(hex)>
UART
MQTT

## Slide 13: Read-only Properties (writable = false)
Azure Cloud
Application MCU
Cloud cannot change read-only properties
Typically used for Application to sync its state information with the cloud
1. Update Property #<x>
property <x>,<new_val>
UART
MQTT
2. New property value is synchronized with the cloud

## Slide 14: Command: Send ASCII Message (from the Cloud)
Azure Cloud
Application MCU
Send ASCII message
(1KB string maximum)
Quick way to send an arbitrary ASCII string from the Cloud to the Application MCU
2. ASCII message echoed on the console
UART
MQTT
NEW

## Slide 15: Using the DTI for Large/Burst Data Transfers
Application MCU
2KB
Bucket #4
Bucket #3
Bucket #2
Bucket #1
2KB
2KB
2KB
Azure IoT Hub
string
string
string
string

## Slide 16: Test Sequence: 8 1KB Strings  4 Data Buckets
Frame No. | Command Byte | Index Byte | Length (MSB) | Length (LSB) | String Data (1024 Bytes)
1 | ‘t’ (0x74) | 0x0B | 0x04 | 0x00 | START1111…1…1…1…1…1…1…1…1…1...1...1…1…1111END
2 | ‘t’ (0x74) | 0x0C | 0x04 | 0x00 | START2222…2…2…2…2…2…2…2…2…2...2...2…2...2222END
3 | ‘t’ (0x74) | 0x0D | 0x04 | 0x00 | START3333…3…3…3…3…3…3…3…3…3...3...3…3...3333END
4 | ‘t’ (0x74) | 0x0E | 0x04 | 0x00 | START4444…4…4…4…4…4…4…4…4…4...4...4…4...4444END
5 | ‘t’ (0x74) | 0x0B | 0x04 | 0x00 | START1111…1…1…1…1…1…1…1…1…1...1...1…1…1111END
6 | ‘t’ (0x74) | 0x0C | 0x04 | 0x00 | START2222…2…2…2…2…2…2…2…2…2…2...2…2...2222END
7 | ‘t’ (0x74) | 0x0D | 0x04 | 0x00 | START3333…3…3…3…3…3…3…3…3…3…3...3…3...3333END
8 | ‘t’ (0x74) | 0x0E | 0x04 | 0x00 | START4444…4…4…4…4…4…4…4…4…4…4...4…4…4444END
Header
Payload
Data Frame
Test Conditions
Disable SAM-IoT light & temperature sensor telemetry reports (set the disableTelemetry property = 3)
Interframe delay = 500 msec
SPI Master SCK = 30 kHz
[Recommendation] Each data frame should be preceded with the CLI command telemetry 0,0
Notes: 1. (5000 milliseconds / 2048 Words) = 2.44 msec per update
2. (5000 milliseconds / 1024 Integers) = 4.88 msec per update

## Slide 17: IoT Central Dashboard – 4 Data Buckets Visualized

## Slide 18: View Raw Data Messages Received by the App
First Received Message
Final Received Message

## Slide 19: SAM-IoT-Wx-v2 Version 1 Available on GitHub
Developers get full MPLAB X projects from Microsoft-owned GitHub repositories
PIC-IoT https://github.com/Azure-Samples/Microchip-PIC-IoT-Wx
SAM-IoT https://github.com/Azure-Samples/Microchip-SAM-IoT-Wx
SAME54-XPRO https://github.com/azure-rtos/samples
PIC32 WFI32E Curiosity TBD (UNDER CONSTRUCTION)
ATSAMA5D27 Wireless SOM TBD (UNDER CONSTRUCTION)
Notes: 4 blocks of 1KB every 5 seconds