## Slide 1: Device Model Summary Model ID = dtmi:com:Microchip:SAM_IoT_Wx_v2;1 File Name = sam_iot_wx_v2-1.json
Type | Name | Schema | Example JSON Message/Format
Telemetry | temperature | integer | {“temperature”:26}
Telemetry | light | integer | {“light”:1369}
Telemetry | button_event | Object | {“button_event”:{“button_name”:“SW0”, “press_count”:7}}
Telemetry | telemetry_Int_1 | integer | {“telemetry_Int_1”:36}
Telemetry | telemetry_Int_2 | integer | {“telemetry_Int_2”:40237}
Telemetry | telemetry_Int_3 | integer | {“telemetry_Int_3”:958}
Telemetry | telemetry_Int_4 | integer | {“telemetry_Int_4”:1069}
Telemetry | telemetry_Dbl_1 | double | {“telemetry_Dbl_1”:12.8767209}
Telemetry | telemetry_Dbl_4 | double | {“telemetry_Dbl_2”:74970.16534}
Telemetry | telemetry_Flt_1 | float | {“telemetry_Flt_1”:620.732195}
Telemetry | telemetry_Flt_2 | float | {“telemetry_Flt_2”:8841.8502}
Telemetry | telemetry_Lng | long | {“telemetry_Lng”:9460867123}
Telemetry | telemetry_Bool | boolean | {“telemetry_Bool”:true}
Telemetry | telemetry_Str_1 | string | {“telemetry_Str_1”:“hello”}
Telemetry | telemetry_Str_2 | string | {“telemetry_Str_2”:“goodbye”}
Telemetry | telemetry_Str_3 | string | {“telemetry_Str_3”:“Message sent…”}
Telemetry | telemetry_Str_4 | string | {“telemetry_Str_4”:“Message received!!!”}

## Slide 2: Device Model Summary Model ID = dtmi:com:Microchip:SAM_IoT_Wx_v2;1 File Name = sam_iot_wx_v2-1.json
Type | Name | Schema | Example JSON Message/Format
Property (Writable) | disableTelemetry | integer | {“disableTelemetry”:{“ac”:200,“av”:84, “ad”:“OK”,“value”:3}}
Property (Writable) | debugLevel | enum | {“debugLevel”:{“ac”:200,“av”:29, “ad”:“success”,“value”:4}}
Property (Read Only) | ipAddress | string | {“ipAddress”:“192.168.1.20”}
Property (Read Only) | firmwareVersion | string | {“firmwareVersion”:“19.7.7.0”}
Property (Read Only) | property_1 | integer | {“property_1”:15}
Property (Read Only) | property_2 | integer | {“property_2”:226}
Property (Writable) | property_3 | integer | {“property_3”:{“ac”:200,“av”:42, “ad”:“success”,“value”:314}}
Property (Writable) | property_4 | integer | {“property_4”:{“ac”:200,“av”:91, “ad”:“OK”,“value”:50}}
Property (Read Only) | led_b | LedState | {“led_b”:1}
Property (Read Only) | led_g | LedState | {“led_g”:2}
Property (Read Only) | led_r | LedState | {“led_r”:3}
Property (Writable) | led_y | LedState | {“led_y”:{“ac”:200,“av”:110, “ad”:“success”,“value”:2}}
Property (Writable) | telemetryInterval | integer | {“telemetryInterval”:{“ac”:200,“av”:55, “ad”:“OK”,“value”:10}}

## Slide 3: Device Model Summary Model ID = dtmi:com:Microchip:SAM_IoT_Wx_v2;1 File Name = sam_iot_wx_v2-1.json
Type | Name | Schema | Example JSON Message/Format
Command (Request) | reboot | Object | {“payload”:{“delay”:“PT5S”}}
Command (Response) | reboot | Object | {“response”:{“status”:“success”,“delay”:5}}
Command (Request) | sendMsg | Object | {“payload”:{“sendMsgString”:“Hello World!!!”}}
Command (Response) | sendMsg | Object | {“response”:{“status”:“received”}}